## Slide 1: POZYX WORKSHOP
Presented by:
Paul Hammond
Professor Stefan Greuter
Deakin University - SCCA

## Slide 2: Aims of this workshop
POZYX
  - What is it?
  - How does it work?
Our Project
  - What is it?
  - How does it work?
  - Demonstration
Future Projects
- Discussion & Brainstorming

## Slide 3: Pozyx – what is it?
Pozyx:
Hardware localisation system
  provides centimetre-accurate positioning and motion information in three-dimensional (3-D) space.

## Slide 4: Pozyx – what is it?
Pozyx:
Utilises ultra-wideband (UWB) wireless radio technology
  Suitable for Indoor and Outdoor use
  No interference with other RF systems (Wi-Fi, TV, Radio, Bluetooth)
  Range:
    Around 30 metres (typical indoor applications)
    Up to 100 metres (with clear line of sight)
  Signals can pass through 1 to 2 walls

## Slide 5: Pozyx – what is it?
Pozyx Hardware:
  Anchors
  Tag(s)
Anchors and Tags measure UWB signal propagation delays
  Ie. How long a signal takes to travel from a sender to a receiver
  Measured in nanoseconds (1 billionth of a second)
  Results in centimetre-accurate positioning

## Slide 6: Pozyx – what is it?
ANCHORS
  Placed in known, fixed locations
    User-defined locations (x, y, z)
  Act as reference points
    enable a Tag to determine its position
    and motion relative to these points
  2-D positioning
    3 Anchors required
  3-D positioning
    4+ Anchors required

## Slide 7: Pozyx – what is it?
TAG(S)
The module(s) we want to track…
Any person or object wearing a tag can be located!
Incorporate:
  3-axis accelerometer
  3-axis gyroscope
  3-axis compass
  Pressure sensor
Multiple Tags can be used within the Pozyx system
  We have 5 available in our kit
Tags can also be used as additional Anchors
  Just remove a jumper on the board
Arduino and Raspberry Pi compatible

## Slide 8: Pozyx – HoW DOES IT WORK?
TRILATERATION
Uses basic geometry to obtain the Tag’s position
  By measuring the distance to a number of Anchors (each with a known position) and finding the intersecting point
  Distance = Speed of UWB signal * Time to reach module
The most commonly used method of positioning
  Eg: Global Positioning System (GPS)
    Satellites = Anchors
    Tag = Your car / phone, etc
Remember:
  2-D positioning
    3 Anchors required (see picture opposite)
  3-D positioning
    4+ Anchors required
    > 4 = greater accuracy

## Slide 9: Our project – what is it?
Our project involves:
Extracting position data (x, y, z) and orientation data (pitch, roll, yaw) from a Pozyx Tag(s)
Streaming that data into a virtual environment (in real-time)
  Unity3D
This lets us physically enter a virtual environment!

## Slide 10: Our project – what is it?
  Entering a virtual environment:
  Our current physical location, orientation and movement is accurately captured by the Pozyx system and mirrored as a Game Object in Unity
  Moving to a particular location, or making a specific gesture, in the physical world can trigger unique responses in the virtual one.
  So, we are able to fully interact with that virtual environment through the utilisation of Unity’s inherent systems, such as object collision detection.

## Slide 11: Our project – HOW IT WORKS?
Software Application:
We’ve developed a Python-based application that:
  Establishes communication with the active Pozyx Anchors and Tag(s)
  Collects positioning (x, y, z) and orientation (pitch, roll, yaw) data, from the Pozyx system, in real-time
  Converts that data into OSC packets and outwardly streams the packets via the OSC protocol
    OSC = Open Sound Control, a lightweight networking protocol
Other applications, such as Unity, can receive OSC packets and extract the position and orientation data
  In Unity, this data can be used to control / manipulate a Game Object

## Slide 12: Our project – HOW IT WORKS?

## Slide 13: Our project – DEMONSTRATION
We will now commence a demonstration of our project…

## Slide 14: Future Projects
We feel this system offers countless opportunities for exciting research / project applications and would now encourage you to engage in a brainstorming discussion to share ideas…
We’ll begin by showing some video demonstrations…

## Slide 15: VIDEO DEMONSTRATION #1

## Slide 16: VIDEO DEMONSTRATION #2

## Slide 17: VIDEO DEMONSTRATION #3